## Slide 1: TROY GROUP Inc.
TROY Group Products and Features Presentation
Pascal Fichet
pfichet@troygroup.com

## Slide 2: TROY Products
Security printers: Printer with secure paper trays
Font cards: MICR, Bar code, OCR and Security fonts
Digitizing : signatures and logo digitizing
TROY toner
  TROY MICR toner
  TROY Security toner / TROY MICR Secure
  TROY indelible solution
  TROY UV Toner / TROY MICR UV toner
MICR printer: check printing
Secure DXi printers: Secured printer to secure high value document
Rx/DX: upgrade kit and printers to secure valuable document
Secure UV printer
Secure Jet printer
TSPE: Software to secure valuable document
TSOM
TCWS
CheckFlow
Check Printing adds-on

## Slide 3: TROY GROUP Inc.
Security Printers

## Slide 4: TROY Products – Security printers
Input tray provides security to prevent unauthorized access to high value paper stock.
Notes: Key locks
Metal plates covers
Locking mechanism between tray and printer

## Slide 5: TROY GROUP Inc.
Font cards

## Slide 6: TROY Products – Font card
DIMM, Compact Flash or USB thumb drive housing TROY PCL5e printer resident fonts - Only visible on outputs
Bar code fonts: UPC-A, UPC-E, EAN-8, EAN-13, BC25, BC39, BC128, POSTNET, POSNET reverse
MICR fonts: E-13B, CMC7
MicroPrint font : 0.6 pt font
Security fonts: ECF, LCF, SCF, Security font, International Convenience Amount (FR, SP, UK)
MISC: OCR A, OCR B, TROY Helvetica reverse

## Slide 7: TROY GROUP Inc.
Digitizing

## Slide 8: TROY Product – Digitizing
From a BMP to a PCL5 printer soft font
DIMM card, compact flash or thumb drive
Comes with the escape sequence, metrics and Windows fonts
Digitizing
a b c d e f
<Esc>(201Q<Esc>(s0p2h72v0s0b201Tabcdef

## Slide 9: TROY GROUP Inc.
TROY toner and indelible solution

## Slide 10: TROY Product – Toner
MICR toner
  Check printing
  Magnetic or optical toner sensing (with TROY printers)
  Works with regular HP printers
  We supply some Lexmark, Xerox, IBM printer models with MICR toner
Security toner
  Special toner forces a bright red stain to appear if chemical alteration is attempted.
MICR toner secure
  MICR toner with Security toner properties (red dye)
Notes: Is the toner filling the lexmark, ibm…a troy toner?
How to call the magnet we glue / white sticker : sensor xxxx?

## Slide 11: TROY Product - Indelible Solution
Indelible solution
  Coating with migration agent to apply on selective areas to secure
  To use WITH TROY Security toner or TROY MICR secure toner for the red dye agent benefit.
  Red bleeding goes through the paper thickness to be visible on the back side of the document. Visible on the front if toner is removed.

## Slide 12: TROY Product – UV toner
UV toner
  Prints black, fluoresce blue under UV light
UV MICR toner
  Prints black, fluoresce blue under UV light
  MICR printing

## Slide 13: TROY Printers
TROY I/O filter firmware
Printer key lock
Toner
cartridge Sensor
HP printer engine
HP Printer
+ paper tray locks
Incoming data stream
PCL5e only
Displays “TROY model Ready”
Modifies default HP settings
Access to TROY settings
  Printer control panel
  TROY printer Utility
Notes: All troy hardware firmware will change the ready message to TROY xxx ready
Modifies default HP settings :
Toner density
Jam recovery
Toner low notification (from warning to stop)
Can use regular HP toner

## Slide 14: TROY GROUP Inc.
MICR Printers

## Slide 15: TROY – MICR Printers – MICR Fonts
E-13B (USA – Canada – UK,…)
CMC7 (Spain, France,…)
Security fonts
MICR hardware fonts

## Slide 16: TROY – MICR printers – Printer key lock
3 position printer key lock
Print MICR
  Job is recognized as MICR job if it includes a call to a TROY MICR font
  Toner sensing : printer checks if a TROY MICR toner cartridge is loaded
Printer Locked
  No job can be printed
MICR Locked
  Regular jobs allowed but MICR jobs

## Slide 17: TROY – MICR Printers – MICR toner sensing
Purpose is to avoid any check printing with regular toner (causing rejection and fees)
On a MICR Job (TROY MICR font called) the printer uses the toner sensor to check if a TROY MICR toner cartridge is loaded
If non TROY cartridge loaded, printer prompts to load TROY MICR toner cartridge or to cancel job
MICR toner sensing

## Slide 18: TROY – MICR Printers – TROYmark
45 degree watermark
Static text and/or captured text from data stream; printing repetitive instances of document info to deter counterfeiting.
Pre-defined and customizable patterns (light, medium, dark, + 3 custom)
Exclusion areas
Any area, front or back side of the page

## Slide 19: TROY – MICR Printers – Other features
Printer PIN codes
Encryption / decryption
User profiles
Audit report
ExptOffset
Secure flash memory for fonts and macro storage
Tray mapping
HP settings
  Disabled jam recovery
  Toner density to 3
  Copies to 1

## Slide 20: TROY GROUP Inc.
Secure DXi Printers

## Slide 21: TROY – DXi Printers – Pantograph
Pantograh / Micro Print border / Warning box
MicroPrint border
  0.6 pt text surrounding an definite area
  Cannot be readable after copy
Pantograph
  Background with an interference pattern hiding words. Words are more visible on copy.
Warning Box
  Customizable text box printed right below a pantograph area

## Slide 22: TROY – Secure DXi printers – Printer key lock
Secure DXi printer : 3 position printer key lock
TROY Secure
  All jobs treated as secured
  Toner sensing : printer checks if a TROY Security toner cartridge is loaded
Printer Locked
  No job can be printed
HP
  Bypasses the TROY firmware

## Slide 23: TROY GROUP Inc.
Rx upgrade kits

## Slide 24: TROY – Rx / DX upgrade kits
Memory card to plug into the printer internal USB or Compact Flash slot
  Compact flash : 4250/4350
  USB thumb drive : 3005, 3015, 4014, 4015, 4515, MFP 4345, M60x
To use in association with TROY Secure Port Monitor software (TROY Port Monitor evolution)
Adding Anti-copy and anti-fraud security features to a document
  Pantograph
  TROYMark
  MicroPrint border
  Warning Box
To secure original document as medical prescriptions, contracts, etc…
  Signature line
  Encryption
  TROY fonts (no MICR font included)

## Slide 25: TROY GROUP Inc.
Secure Rx Printers
HP printer + TROY Rx functions embedded
LJ 3015, M60x

## Slide 26: TROY SecureUV Printer.
TROY SecureUV Printer
Black and white and UV
Dedicated color will print UV
Technology LED, high resolution
Compact desktop size

## Slide 27: TROY SecurePro Jet
TROY SecurePro Jet
Inkjet color

## Slide 28: TROY - TSPE
TROY Secure Print Enterprise
Rx / DX security features integrated into a software
Software captures the job and add security features then route it to a printer.

## Slide 29: TROY - TSOM
Print engine
  Raw data are copied into a folder
  TSOM pick up the file
  Parse the data
  Merge the data with a template
  Add the TROY security features
  Send it to the printer fleet
When?
  Customer has data to print into an elaborate template automatically.
  No user interface needed, works in the background
TROY Secure Output Manager

## Slide 30: TROY - TCWS
English only
Windows 7 only
User Interface
Signature cards
Manual checks
When?
  Customer has data to print into an elaborate template.
  Needs for user interface, user roles and permissions, approvals, logs
TROY CheckWriting Software
Check Printing Software

## Slide 31: TROY - Secure CheckFlow
Web application
User Interface
Manual checks
When?
  Big deals
  Customer has data to print into an elaborate template.
  Needs for user interface, user roles and permissions, approvals, logs
Secure CheckFlow
Check Printing Software

## Slide 32: TROY - Check Printing
When?
  Customer needs an add-on to Sage 50 or QuickBooks to print checks
TROY CheckPrinting
Sage 50
Quickbooks